## Slide 1
J. M. Martins Ferreira
University of Porto (FEUP / DEEC)
Rua dos Bragas - 4099 Porto Codex - PORTUGAL
( jmf@fe.up.pt )
BST reuse beyond structural test: Extending the application domain of this test technology
(part 3)
Leonardo INSIGHT II
CoDeVer Meeting
HIBU, September 21st, 1998

## Slide 2: Outline of the presentation (afternoon)
Review of BS concepts (IC and PCB levels)
Extending the application domain of BST / Introduction to prototype debugging and validation through BS
Lunch break
Prototype debugging and validation through BS / Real-time fault detection
Parametric testing through BS / The 1149.4 proposed standard for mixed-signal testing

## Slide 3: Part 3: Outline
Prototype debugging and validation through BS / Real-time fault detection
  A small application example
  Optional BS instructions to support prototype debugging and validation
  Design for debug and test
  Feasibility aspects
Real-time fault detection through BS
Prototype debugging and validation

## Slide 4: Example: Debugging a simple double sequence detector FSM
Output Z indicates when the sequence 101 takes place simultaneously in both inputs (X,Y)
Overlapping sequences are to be detected as well (10101 will activate Z twice)
Prototype debugging and validation

## Slide 5: Debugging set up using the dual-processor controller model
Prototype debugging and validation

## Slide 6: Excerpt from the double sequence FSM debugging program
Prototype debugging and validation
...
CPUCLF:
CPUCLT:
...
seltap0
wsa1
setout 0
ssa1
wsa1
rstout 0
jnz 0,error
setout 1
clk
setout0
ssa0
ld c16,2
ncshfcp
.db $00,$03
jpe errorclt
ssa1
wsa0

## Slide 9: Optional BS instructions (design for debuggability)
Optional BS instructions help to overcome the speed limitations of hardware debugging via scan
The dual-processor debugging controller model previously presented may still be used when only the mandatory IEEE 1149.1 instructions are available, but at the cost of a degraded debugging performance
The optional BS instructions defined support BP and RT debug operations
Prototype debugging and validation

## Slide 10: Optional BS instructions to support BP and RT
Breakpoint: The optional BS instructions enable automatic detection of the BP condition through the BS register
Real-time: Optional BS instructions use the BS register to
  Store two consecutive vectors
  Store two consecutive vectors after a pre-specified circuit condition takes place
  Store two consecutive vectors until a pre-specified circuit event takes place
Prototype debugging and validation

## Slide 11: Optional BS instructions: Automatic detection of BP conditions (1)
Prototype debugging and validation
Objective: To activate a dedicated output pin upon the occurrence of a given circuit condition (single or multiple component)
Additional resources required:
  Two optional BS instructions (Sel_cond, Det_cond)
  A modified BS cell structure (detection of the BP condition takes place in the BS cells)
  Two additional pins in each BS IC: CDI (condition detection input) and CDO (... output), used for cascading and to interface the debug controller

## Slide 12: Optional BS instructions: Automatic detection of BP conditions (2)
Prototype debugging and validation
Optional BS instructions Sel_cond, Det_cond:
  Sel_cond selects a 3-bit register (8 conditions)
  The mandatory S / P instruction is used to store the expected values in the update stages
  Det_cond is then used to shift the mask data into the shift / capture stage
  The BS cells are not modified in Capt-DR or Upd-DR, when Det_cond is the current instruction
  The condition is evaluated in the RT / I state and the result is output at the CDO pin

## Slide 13: Optional BS instructions: Automatic detection of BP conditions (3)
Prototype debugging and validation
Modified BS cell structure:

## Slide 14: Optional BS instructions: RT — Store two vectors (1)
Prototype debugging and validation
Objective: To capture two consecutive vectors and to store them in the shift / capture and update stages
Additional resources required:
  One optional BS instruction (Store_seq)
  A modified BS structure
A larger number of vectors may be stored by adding latch stages to the modified BS cells

## Slide 15: Optional BS instructions: RT — Store two vectors (2)
The optional BS instruction Store_seq:
  The first vector is captured into the shift / capture stages on the rising edge of TCK (on RT / I)
  The next rising edge of TCK captures the second vector and takes the TAP controller to Sel.-DR scan
  The first vector is read on the Shift-DR state (the shift / capture stage does not change on Capt.-DR)
  The TAP controller is taken through Pause-DR / Exit-2 DR (where the contents of the update stage are captured into the shift / capture stage) / Shift-DR, which enables the second vector to be read
Prototype debugging and validation

## Slide 16: Optional BS instructions: RT — Store two vectors (3)
Prototype debugging and validation
Modified BS cell structure:

## Slide 17: Optional BS instructions: RT — Store two vectors (4)
Prototype debugging and validation
Timing diagram:

## Slide 18: Optional BS instructions: RT — Store two vectors after condition (1)
Prototype debugging and validation
Objective: To merge condition detection and consecutive vector storage
Additional resources required:
  One optional instruction (Store_after_cond)
  A modified BS cell structure and a finite state machine (FSM) with 4 states (monitor condition, capture sequence I and II, end of sequence)
  Two additional pins in each BS IC: CDI and CDO
A larger number of vectors may be stored by adding latch stages to the modified BS cells

## Slide 19: Optional BS instructions: RT — Store two vectors after condition (2)
The optional BS instruction Store_after_seq:
  Set up as for the Det_cond BS instruction
  Assuming the FSM in “monitor sequence”, TAP controller in RT / I, and that a detection event took place, transitions on TCK have the following effect:
    Falling: The FSM goes to “capture sequence I”
    Rising: Captures the first vector into the S/C stages
    Falling: Transfers the contents of S/C to UPD stages and the FSM to “capture sequence II”
    Rising: Captures the second vector into the S/C stages
    Falling: Takes the FSM to “end of sequence” and enables the vectors to be read as with the Store_seq instruction
Prototype debugging and validation

## Slide 20: Optional BS instructions: RT — Store two vectors after condition (3)
Prototype debugging and validation
Modified BS cell structure:

## Slide 21: Optional BS instructions: RT — Store two vectors after condition (4)
Prototype debugging and validation
Timing diagram:

## Slide 22: Optional BS instructions: RT — Store two vectors until CDI (1)
Prototype debugging and validation
Objective: To capture and store two-vector sequences until the CDI pin is asserted
Additional resources required:
  One optional BS instruction (Store_until_CDI)
  A modified BS cell structure and a FSM with two states (monitor condition and end of sequence)
  Two additional pins in each BS IC: CDI and CDO
A larger number of vectors may be stored by adding latch stages to the modified BS cells

## Slide 23: Optional BS instructions: RT — Store two vectors until CDI (2)
The optional BS instruction Store_until_CDI:
  Assuming the FSM in “monitor condition” and the TAP controller in RT / I, each rising edge on TCK captures a new vector into the S/C stage and each falling edge transfers the contents of S/C to UPD
  When CDI is asserted the FSM goes to “end of sequence” on the falling edge of TCK
  The two vectors may be read as with Store_seq
The modified BS cell structure proposed for Store_seq also supports Store_until_CDI
Prototype debugging and validation

## Slide 24: Optional BS instructions: RT — Store two vectors until CDI (3)
Prototype debugging and validation
Timing diagram:

## Slide 25: A general design for debug and test framework
Prototype debugging and validation

## Slide 26: Cost / benefit reasoning...
On-board / on-chip controller architectures as the one discussed, combined with optional BS instructions in some ICs, have pros and cons…
Silicon and packaging overhead (cost) are easy to measure, but the advantages of extending the usefulness of the BS infrastructure (benefit) is hard to estimate
Prototype debugging and validation

## Slide 27: Texas Instruments
Prototype debugging and validation

## Slide 28: Corelis
Prototype debugging and validation

## Slide 29: Göpel electronic GmbH
Prototype debugging and validation

## Slide 30: Real-time fault detection
Fault tolerance is enabled by redundancy: spatial (hardware), informational (data structures) or temporal (computation)
Redundancy implies lower speed (temporal / informational redundancy), higher cost (spatial redundancy) or both (in most cases)
Scan-based real-time fault detection and containment may play an important role in the introduction / enhancement of fault-tolerant features
Real-time fault detection

## Slide 31: Real-time fault detection: Overview of a possible solution
Real-time fault detection

## Slide 32: Modified BS cells
Real-time fault detection

## Slide 33: Faulty condition registers
Real-time fault detection

## Slide 34: Control register
Real-time fault detection

## Slide 35: Optional instructions required
Real-time fault detection

## Slide 36: Modified TAP controller diagram
Real-time fault detection

## Slide 37: On-line fault detection FSM
Real-time fault detection

## Slide 38: Synchronisation with the system CLK
Real-time fault detection

## Slide 39: Fault output FSM for sequences of illegal values
Real-time fault detection

## Slide 40: Coffee break