## Slide 1
J. M. Martins Ferreira
University of Porto (FEUP / DEEC)
Rua dos Bragas - 4099 Porto Codex - PORTUGAL
( jmf@fe.up.pt )
Leonardo INSIGHT II
CoDeVer Meeting
HIBU, September 21st, 1998
BST reuse beyond structural test: Extending the application domain of this test technology
(part 1)

## Slide 2: Outline of the presentation (morning)
Review of BS concepts (IC and PCB levels)
Extending the application domain of BST / Introduction to prototype debugging and validation through BS
Lunch break
Prototype debugging and validation through BS / Real-time fault detection
Parametric testing through BS / The 1149.4 proposed standard for mixed-signal testing

## Slide 3: Motivation
BS is traditionally used for structural testing of digital PCBs in a production test environment
The general question underlying this seminar consists of deciding if it would be of interest:
  To widen its application domain (e.g. functional testing, parametric testing)?
  To reuse this test technology in other stages during the product life cycle?
Introduction

## Slide 4: BS and the product life cycle
In other words, what modifications would result to the diagram below if:
  An extended BS infrastructure (supporting optional instructions) was available?
  An on-board controller was available?
  An extended BS infrastructure (supporting additional test structures) was available?
Introduction

## Slide 5: Part 1: Outline
BST at IC level: The BS architecture and test access port
BS at PCB level: Test protocol and test controller model
Application example: Non-BS cluster testing through PRPG / PSA
Review of BS concepts

## Slide 6: The BS architecture and TAP
Besides the BS register, the test logic includes additional data registers, an instruction register and a TAP controller finite state machine
Review of BS concepts

## Slide 7: Access protocol to the BS architecture
The TAP controller places the instruction register in the TDI-TDO path
A bit sequence (instruction) is shifted in, setting the contents of the instruction register to select the required data register
The TAP controller places the selected data register in the TDI-TDO path
Test vectors may now be shifted in and out through the selected test data register
Review of BS concepts

## Slide 8: The basic BS cell
Three main operating modes:
  Transparent
  Controllability
  Observability
Review of BS concepts

## Slide 9: BS: The basic test protocol
Shift in a new test vector (left mux in Shift mode, right mux in Normal or Test modes)
Apply the test vector (left mux in Shift or Capture modes, right mux in Test mode)
Capture the responses (left mux in Capture mode, right mux in Normal or Test modes)
Shift out the responses (left mux in Shift mode, right mux in Normal or Test modes)
Review of BS concepts

## Slide 10: The instruction register: Mandatory instructions (1)
The EXTEST instruction selects the BS register and imposes the (external) test mode in each BS cell, decoupling the IC core logic from the pins (the EXTEST instruction has a pre-defined code of all-0s)
The SAMPLE / PRELOAD instruction also selects the BS register, but the BS cells are now in transparent mode (this instruction does not have a pre-defined code)
Review of BS concepts

## Slide 11: The instruction register: Mandatory instructions (2)
Both EXTEST and SAMPLE / PRELOAD are used to test the board interconnects, but S/P is used to shift in the first test vector (why?)
The BYPASS instruction selects the 1-bit bypass register in those ICs which do not play a role in the current test operation (this instruction has an all-1 code and is automatically loaded into the IR on reset)
Review of BS concepts

## Slide 12: TAP controller state diagram
Review of BS concepts

## Slide 13: A BS test controller
The BS test controller model that will be presented in the next slides has the following objectives:
  To identify the main information sources required for test program generation
  To present a formal (yet simple) specification language to write small test programs
  To provide a tool for test program validation
  To enable hands-on sessions
Review of BS concepts

## Slide 14: Instructions to control the BS infrastructure
Review of BS concepts

## Slide 15: Instructions for synchronisation with external test resources
Review of BS concepts

## Slide 16: Instructions to control internal test resources and test flow
Review of BS concepts

## Slide 17: Test set up
A PC running Windows 95, a 5 V power supply, the demonstration board and the flat-cable connector
Review of BS concepts

## Slide 18: Review of BS concepts: Case study
Testing the IC1+IC2 cluster via PRPG / PSA
Review of BS concepts

## Slide 19: Coffee break