## Slide 1
J. M. Martins Ferreira
University of Porto (FEUP / DEEC)
Rua dos Bragas - 4099 Porto Codex - PORTUGAL
( jmf@fe.up.pt )
BST reuse beyond structural test: Extending the application domain of this test technology
(part 2)
Leonardo INSIGHT II
CoDeVer Meeting
HIBU, September 21st, 1998

## Slide 2: Part 2: Outline
Extending the application domain of BST beyond structural testing
  Possible application areas
  Limitations of the current 1149.1 standard
Introduction to prototype debugging and validation through BS
  A debug and test controller model
A BS test controller

## Slide 3: An extended application domain
What would prevent the BS infrastructure to be used for:
  Functional testing
  Prototype debugging and validation
  Real-time fault detection
  Parametric testing
  Mixed-signal testing
Extending the application domain of BS

## Slide 4: Functional testing
Goal: To check that the circuit (IC, PCB, etc.) function is as expected
Main limitations:
  Synchronisation between test and system logic
  Predicting what values are to be captured
  Repeatability of the test sequence
  Sampling at representative CLK frequencies
  Need to cope with processor-based or dedicated hardware -based solutions
  ...
Extending the application domain of BS

## Slide 5: Prototype debugging and validation
Goal: To detect structural and functional faults, avoiding in-circuit access (in-circuit emulators, logic probes, …)
Main limitations:
  Similar to functional testing, since structural testing operations are easily achieved through the BS infrastructure
Extending the application domain of BS

## Slide 6: Real-time fault detection
Goal: To enhance circuit reliability and add fault tolerance features
Main limitations:
  Similar to functional testing, in terms of synchronisation, prediction of captured values, speed of operation, etc.
  Coverage of defect conditions
  To provide recovery / graceful degradation solutions
  ...
Extending the application domain of BS

## Slide 7: Parametric testing
Goal: To verify parametric information (propagation and transition times, input / output voltage and current values, …)
Limitations:
  Synchronisation between relevant event and TCK
  Speed (TCK frequencies versus propagation or transition times)
  Analogue nature of voltage and current parameters
  ...
Extending the application domain of BS

## Slide 8: Mixed-signal testing
Goal: To enable the BS infrastructure to deal with analogue signals
Limitations:
  The digital nature of the IEEE 1149.1 standard
  The structural test nature of the IEEE 1149.1 standard
Solution: The P1149.4 standard
Extending the application domain of BS

## Slide 9: A (simplified) debugging model
Prototype debugging and validation
SS: Single-step
RT: Real-time operations
BP: Breakpoints
COV: Controllability, observability and verification operations
CIT: Control of internal resources and test program flow

## Slide 10: Definition of a debugging controller model
Hardware debugging via a scan infrastructure versus traditional in-circuit emulators (ICEs):
  The number of pins available for controllability / observability is much larger
  Speed may be slower, due to the serial nature of scan operations
Splitting test and debug operations enables an easy to expand model and may improve speed through concurrent execution
Prototype debugging and validation

## Slide 11: A dual-processor built-in controller model for debug and test
Prototype debugging and validation

## Slide 12: CPUCLF: Basic operations and instructions to support SS
Prototype debugging and validation
Instructions to support SS operations:
Single-stepping may be implemented by controlling the number of clock cycles applied to the system

## Slide 13: CPUCLF: Basic operations and instructions to support BP
Instructions to support BP operations:
Prototype debugging and validation
Breakpoint operating modes may be implemented by conditionally applying clock cycles to the system
Optional BS instructions may improve the BP operations supported

## Slide 14: CPUCLF: Basic operations to support RT
Prototype debugging and validation
Real-time operating modes may be implemented by:
  Controlling the system clock start and stop times
  Enabling “cycle stretching”: Repeat the application of N clock cycles, stretching one cycle in each run — start with the first clock cycle, stop when a time-dependent error is eliminated or the last of the possible N2 clock cycles is applied
Optional BS instructions may improve the RT operations supported

## Slide 15: CPUCLF: Instructions supporting RT operations
Prototype debugging and validation

## Slide 16: CPUCLF: Basic operations to support COV
Controllability, observability and verification operations refer to directly accessible pins (parallel I/Os):
  Control the logic level of an output pin
  Select (for observation) one of the input pins
  Enable conditional actions according to specific circuit conditions
Prototype debugging and validation

## Slide 17: CPUCLF: Instructions supporting COV operations
Prototype debugging and validation

## Slide 18: CPUCLF: Basic operations to support CIT
If a dedicated processor architecture is used to implement this instruction set, additional operations for controlling internal resources and program flow are required:
  Operations related to an internal counter
  Synchronisation with external test equipment or other on-board controllers
  Operations to control program execution flow (conditional, re-direction and stop)
Prototype debugging and validation

## Slide 19: CPUCLF: Instructions supporting CIT operations
Prototype debugging and validation

## Slide 20: Example of a simple CPUCLF program
Prototype debugging and validation
...
cnt: setout 1 ; reset...
clk ; ... counter
rstout 1 ; disable reset
setout 0 ; enable counter
clk_n 15 ; 15 clock cycles
jz in0,error ; RCO not active?
...

## Slide 21: CPUCLT: Additional test controller instructions
Prototype debugging and validation

## Slide 22: Lunch break