## Slide 1
The Boundary Scan Test (BST) technology
J. M. Martins Ferreira
(jmf@fe.up.pt)
FEUP / DEEC - Rua dos Bragas
4099 Porto Codex - PORTUGAL
Tel. 351-1-2041748 / Fax: 351-2-2003610

## Slide 2: Objectives
To present in detail the BS test technology, emphasising its implementation and application domain
To enable the student to acquire sufficient knowledge to design and implement a simple BS architecture

## Slide 3: Outline
The development of BS and its application domain
The BS architecture and test access port (TAP)
  The basic BS cell
  The test data registers
  The instruction register
  The TAP controller state machine

## Slide 4: Why Boundary Scan Test?
The two main reasons that led in the mid-80s to the development of BST were:
  The increasing complexity of integrated circuits (ICs) made it exceedingly difficult to develop test programs for the functional test of complex printed circuit boards (PCBs)
  The shrinking effect of using small outline surface mount devices and advanced mounting technologies almost disabled physical access to internal PCB nodes and made in-circuit test exceedingly difficult

## Slide 5: The application domain of BST
BST addresses the structural test of digital printed circuit boards
Keywords: structural, digital, PCBs
The narrow scope of BST contributed to its acceptance and to the quick development of products, but the potential of a standard embedded test infrastructure goes much beyond the initial application domain

## Slide 6: The basic concept of BST
BS makes it possible to decouple the internal IC logic from the pins and allows “direct” access to any PCB node without backdriving effects

## Slide 7: The Test Access Port (TAP)
TDI (Test Data Input): The serial data input to the BS register (a floating TDI is read as a 1)
TDO (Test Data Output): The serial data output of the BS register (in high-impedance except when a scan operation is in progress)
TCK (Test Clock): Clock for the test logic
TMS (Test Mode Select): A control input that defines the operating mode required for the test logic (a floating TMS is read as a 1)

## Slide 8: The BS architecture
Besides the BS register, the test logic includes additional data registers, an instruction register and a TAP controller finite state machine

## Slide 9: Access protocol to the BS architecture
The TAP controller places the instruction register in the TDI-TDO path
The proper bit sequence (instruction) is shifted in, setting the contents of the instruction register to select the required data register
The TAP controller places the selected data register in the TDI-TDO path
Test vectors may now be shifted in and out through the selected test data register

## Slide 10: The basic BS cell
Three main operating modes:
  Transparent
  Controllability
  Observability

## Slide 11: BS: The basic test protocol
Shift in a new test vector (left mux in Shift mode, right mux in Normal or Test modes)
Apply the test vector (left mux in Shift or Capture modes, right mux in Test mode)
Capture the responses (left mux in Capture mode)
Shift out the responses (left mux in Shift mode)

## Slide 12: Is BS test slow?
Scanning in and out each test vector / responses may be unacceptable for IC test, which may require hundreds of thousands of vectors
However, and considering the main application domain of BS (structural testing of PCBs), we shall see that the number of test vectors required is normally small

## Slide 13: BS: The test data registers (1)
The BS register comprises the set of BS cells present in the circuit and is mandatory in any BS IC (at least two instructions selecting this register have to be supported: EXTEST and SAMPLE / PRELOAD)
The bypass register is mandatory and its function is to shorten the total length of the serial PCB-level chain (it has a single bit and is selected by the BYPASS instruction)

## Slide 14: BS: The test data registers (2)
The identification register is optional and its function is to provide a 32-bit sequence enabling the test engineer to perform an identity check on each device supporting the IDCODE instruction
The user test data registers are also optional and will normally interface additional testability infrastructures introduced by the designers

## Slide 15: The instruction register: Mandatory instructions (1)
The EXTEST instruction selects the BS register and imposes the (external) test mode in each BS cell, decoupling the IC core logic from the pins (the EXTEST instruction has a pre-defined code of all-0s)
The SAMPLE / PRELOAD instruction also selects the BS register, but the BS cells are now in transparent mode (this instruction does not have a pre-defined code)

## Slide 16: The instruction register: Mandatory instructions (2)
Both EXTEST and SAMPLE / PRELOAD are used to test the board interconnects, but S/P is used to shift in the first test vector (why?)
The BYPASS instruction selects the bypass register and enables a 1-bit data path through those ICs which do not play a role in the current test operation (this instruction has an all-1 code and is automatically loaded into the instruction register on reset)

## Slide 17: The TAP controller
The TAP controller is a small finite state machine that generates most of the control signals required by the BS architecture
The TAP controller commands the register placed between TDI and TDO to...
  capture the logic value present at the parallel input of its cells
  shift data serially through the register cells
  update the cell parallel outputs with the values that were shifted in

## Slide 18: TAP controller state transition diagram

## Slide 19: The TAP controller states (1)
Capture, Shift and Update (-DR or -IR) are the states where the selected register performs the three main test operations
In the Test Logic Reset the BS register is in transparent mode and the functional logic operating normally
Run Test / Idle is used to perform certain test operations (such as BIST — Built-In Self-Test)

## Slide 20: The TAP controller states (2)
Select, Exit1 and Exit2 (-DR or -IR) are temporary states
Exit1 and Exit2, combined with Pause (-DR or -IR) allow shifting of test data to be temporarily halted
The Select states allow selection of which type of register (-DR or -IR) to place between TDI and TDO

## Slide 21: TAP controller timing details
State transitions occur with the rising edge in the TCK signal
Actions in a TAP controller state (such as capture, shift or update operations) occur with the falling edge of TCK in the state

## Slide 22: BSDL: Boundary Scan Description Language
BSDL is a subset of VHDL that describes the BS infrastructure and its operation (approved as IEEE std. 1149.1b in 1994)
Mandatory features are not described in BSDL (e.g. a BSDL description does not describe the BYPASS register)
CAD tools making use of BSDL: testability analysis, automatic test pattern generation, fault diagnosis, etc.

## Slide 23: HSDL: Hierarchical Scan DL and SVF: Serial Vector Format
HSDL complements BSDL, describing how IEEE 1149.1 is implemented at board level
SVF was jointly developed by Teradyne and Texas Instruments to enable a vendor-independent representation of IEEE 1149.1 test patterns
An SVF file contains ASCII statements consisting of commands and parameters of 3 types: state, offset and parallel commands

## Slide 24: Coffee break

## Slide 25: The Scan Educator application (TI)

## Slide 26: A demo BS IC on a PAL (“IEEE 1149.1-like”)

## Slide 27: Lunch break