## Slide 1: Basic test concepts
J. M. Martins Ferreira
(jmf@fe.up.pt)
FEUP / DEEC - Rua dos Bragas
4099 Porto Codex - PORTUGAL
Tel. 351-1-2041748 / Fax: 351-2-2003610

## Slide 2: Objectives
To emphasise the importance of testing in the overall product development cycle
To introduce the basic concepts in testing and design for testability
To prepare the student to understand in detail the standard boundary scan test architecture

## Slide 3: Outline
Fault modeling and ss@ faults
Controllability, observability and testability
Test vector generation for combinational circuits
Testability and test generation in sequential circuits
Testability improvement via ad hoc solutions
Structured approaches to design for testability

## Slide 4: The importance of testing
No testing, no manufacturing
Cost of testing is very high, but the cost of defective testing strategies is even higher
Available test standards
A brief historical perspective

## Slide 5: Why fault models?
Possible physical defects are too many and defect spectrum too wide
Effective test strategies require that the complexity of considering possible malfunction causes is reduced to an acceptable level
Fault models are an abstract representation of defective circuit conditions (a fault is at logic level, a defect is at physical level)

## Slide 6: Attributes of a good fault model
Simplicity, to allow efficient test vector generation procedures
Defect coverage, to guarantee that the percentage of defective components escaping detection is acceptably low

## Slide 7: The single stuck-at fault model
A structural fault model assuming that
  Only one node at a time is faulty
  Only two types of faults: s@0 and s@1
Experience has shown that the ss@ fault model has excellent characteristics concerning the attributes previously referred

## Slide 8: Controllability of a node

## Slide 9: Problems due to low controllability
Low controllability leads to difficult test vector generation, since:
  Our first step to detect a given s@ fault in a node consists of driving it to a logic value that is the opposite of the fault
  In an IC, the value at any node can only be controlled from the input pins (the primary inputs of the circuit)
Low observability, as we shall see, has a similar effect

## Slide 10: Observability of a node

## Slide 11: Testability
Testability is a combined measure of controllability and observability
High testability facilitates test vector generation and leads to better test effectiveness
So, why aren’t all circuits highly testable?

## Slide 12: The D-notation
Used in the test vector generation D-algorithm, introduced by Paul Roth in the mid-60s
D is a composite logic value that results from driving a s@0 node to 1 (and /D its dual)

## Slide 13: The D-algorithm
Drive the node to a logic value that is the opposite of the fault (0 if s@1 and 1 if s@0)
Propagate the error signal (D or /D) to a primary output
Justify (backwards) the values that enable the propagation path, until a necessary combination at the primary inputs (a test vector) is found

## Slide 14: A test generation example

## Slide 15: The case of undetectable faults

## Slide 16: Backtracking

## Slide 17: Test generation for sequential circuits
Direct application of the D-algorithm leads to the combinational block inputs and outputs, not necessarily to primary inputs or outputs

## Slide 18: Test generation - step 1

## Slide 19: Test generation - step 2

## Slide 20: Test generation - step 3

## Slide 21: The complexity of the general case is however much higher, because...
The D-algorithm does not necessarily lead to circuit primary inputs and outputs
Knowledge of the circuit state transition diagram is required
The fault may indeed affect the state transition diagram, in which case the determination of the required sequence at the circuit primary inputs becomes even more difficult

## Slide 22: Take the example of Y s@0...

## Slide 23: Ad hoc testability improvements
Design rules or amendments to avoid or minimise test vector generation problems
Major drawbacks:
  Not always reusable
  Testability depends largely on the type of circuit

## Slide 24: Some ad hoc testability rules
Split counters to avoid high numbers of clock cycles until the required output combination is achieved
Include reset and preset lines (synchronous or asynchronous)
Partition large circuits and add extra inputs and outputs for direct controllability and observability of internal nodes

## Slide 25: Structured Design for Testability (DfT) methodologies
The objective of structured DfT methodologies is to enable a simple way to drive the circuit to any given state in a fixed (and short) number of clock cycles
Does structured DfT have drawbacks?
  Design rules (or rather a design style) have to accepted
  Additional silicon area, more pins and higher propagation delays… but is this an additional cost?

## Slide 26: The scan design principle
The scan design principle consists of inserting a 2:1 multiplexer between the input of every D flip-flop and its driving logic

## Slide 27: Advantages of scan design (1)
Problem: Part of the combinational circuitry inputs are not directly controllable, since they come from the D-FF outputs (these nodes define the circuit present state)
Solution: The scan flip-flops shown in figure 1.9 enable direct controllability of the D-FF outputs through a simple procedure with a fixed number of clock cycles

## Slide 28: Better controllability through scan design (1)

## Slide 29: Better controllability through scan design (2)

## Slide 30: Better controllability through scan design (3)

## Slide 31: Better controllability through scan design (4)

## Slide 32: Better controllability through scan design (5)

## Slide 33: Advantages of scan design (2)
Problem: Part of the combinational circuitry outputs are not directly observable, since they go to the D-FF inputs (these nodes define the circuit next state)
Solution: The scan flip-flops shown in figure 1.9 enable direct observability of the D-FF inputs through a simple procedure with a fixed number of clock cycles

## Slide 34: Better observability through scan design (1)

## Slide 35: Better observability through scan design (2)

## Slide 36: Better observability through scan design (3)

## Slide 37: Better observability through scan design (4)

## Slide 38: Better observability through scan design (5)

## Slide 39: DfT: Eventually an overhead
The 2:1 multiplexers increase the propagation delay and required additional silicon area and more pins, but this does not necessarily mean higher cost
Benefits due to easier test vector generation and application are difficult to quantify
Design freedom was traded for higher testability, but partial scan design might be a preferred intermediate solution