## Slide 1: Test protocol for BS boards
J. M. Martins Ferreira
(jmf@fe.up.pt)
FEUP / DEEC - Rua dos Bragas
4099 Porto Codex - PORTUGAL
Tel. 351-1-2041748 / Fax: 351-2-2003610

## Slide 2: Objectives
To enable the student to understand the main issues that have to be considered when testing a board with BS
To present a test protocol that covers the main test actions required
To emphasise insufficiencies in this test protocol and identify the steps requiring further attention

## Slide 3: Outline
Fault detection in the BS infrastructure
Open and short-circuit fault detection in full-BS interconnects
Full-BS interconnects testing in boards with multiple BS scan chains
Fault detection in non-BS clusters
Testing non-BS clusters in boards with multiple BS scan chains
Faulty components detection

## Slide 4: The test protocol
Integrity check of the BS infrastructure
Full-BS interconnects test
  Open fault detection
  Short-circuit fault detection
Non-BS clusters testing
Components test
  Components with BIST
  “Dead or alive” test in non-BIST components

## Slide 5: Integrity check of the BS infrastructure
Detection of:
  Faulty TAP pins
  Faulty / misplaced components
Sequence of operations:
  Reset (TRST or 5 x TMS1)
  IR capture and scan
  ID capture and scan

## Slide 6: Open fault detection in full-BS interconnects
The test vectors drive both a 0 and a 1 through each driving pin in each interconnect
Insert the SAMPLE / PRELOAD instruction and shift in the first test vector
Insert EXTEST and apply the remaining test vectors

## Slide 7: Short-circuit fault detection in full-BS interconnects
Test principle: Drive the interconnects under test to opposite logic values
Short-circuits are potentially destructive and the number of possible faults grows exponentially with the circuit dimension
Fault detection is much simpler that fault diagnosis, since any multiple interconnect shorts will be detected if all two-interconnect shorts are detected

## Slide 8: The binary partition algorithm for short-circuit test vector generation
The binary partition algorithm guarantees complete fault detection with a minimum number of test vectors (and minimum diagnostic resolution…)

## Slide 9: Full-BS interconnect testing in boards with multiple BS chains
Easier in the case of open fault detection
Short-circuit fault detection requires a co-ordinated protocol:
  Shift the test vector in through the BS register cells and proceed to the update-DR and select-DR TAP controller states after the last bit is shifted in
  Repeat this operation with all remaining BS chains
  Capture the test vector responses present in the first BS chain (move on to the Capture-DR state)
  Repeat this operation with all remaining BS chains

## Slide 10: Fault detection in non-BS clusters: Full in-circuit access
Highest requirements in external test resources
Maximum speed

## Slide 11: Fault detection in non-BS clusters: Peripheral access
Intermediate solution in terms of required external test resources and speed

## Slide 12: Fault detection in non-BS clusters: Primary I/O access only
Slowest (when a set of deterministic test vectors is to be used)
Cheapest (no external test resources required, besides the primary I/O test channels)

## Slide 13: Test vector generation
Test generation is done by an automatic test pattern generation tool, according to a specific fault model and to the test resources assumed to be available
Notice however that pseudo-random pattern generation (PRPG) and signature analysis (SA) may be used in certain cases and provide an effective and very fast test alternative

## Slide 14: Non-BS clusters testing in boards with multiple BS chains
The first two test set up alternatives (full in-circuit access and peripheral access) pose no special requirements, since the BS chains are not used or play a minor role
When external test resources are available only for the cluster primary I/O pins, the test protocol is the same that was described for short-circuit fault detection in full-BS interconnect testing

## Slide 15: Components testing
Due to the main application domain of BS, limited facilities are to be expected for components testing
Complex VLSI circuits will normally include BIST structures, accessible through the RUNBIST instruction
The remaining cases are limited to a simple “dead or alive” test with the EXTEST or INTEST instructions