## Slide 1: A BS test controller model
J. M. Martins Ferreira
FEUP / DEEC - Rua dos Bragas
4050-123 Porto - PORTUGAL
Tel. 351-22-2041748 / Fax: 351-22-2003610
(jmf@fe.up.pt / http://www.fe.up.pt/~jmf)

## Slide 2: Objectives
To identify what are the main information sources required to enable test program generation for BS boards
To present a formal (yet simple) specification language that enables the student to write test programs for real case studies

## Slide 3: Outline
Basic test operations
  To control the BS infrastructure
  To synchronise the BS infrastructure with external test resources
  To control internal test resources and test program flow
The test instruction set for each type of basic test operations
Test program generation

## Slide 4: Basic test operations to control the BS infrastructure (1)
Apply an active-low pulse in /TRST
Apply a TCK cycle while TMS is fixed at a pre-defined (0 or 1) logic value
Shift a bit stream into the selected scan chain, without comparing the bits shifted out with any expected responses (the TMS line must be held at 0 except in the last TCK cycle, when it must be held at 1)

## Slide 5: Basic test operations to control the BS infrastructure (2)
Shift a bit stream into the selected scan chain, while the bit stream shifted out is checked against expected values in pre-defined bit locations (the TMS line must be held at 0 except in the last TCK cycle, when it must be held at 1)
Apply N TCK cycles while TMS is held at 0
Select the BS chain in which the following test operations are to take place

## Slide 6: Basic test operations for synchronisation purposes
Set the synchronisation output to a pre-defined logic value (0 or 1)
Wait until the synchronisation input is set to a pre-defined logic value (0 or 1)

## Slide 7: Basic test operations to control internal resources and test flow
Load an internal counter with the required number of TCK cycles
Select the error flag to be set if an expected value is not found
Perform a conditional jump in the test program flow according to the value of the selected error flag
Conclude the test program

## Slide 8: Instructions to control the BS infrastructure

## Slide 9: The bit stream in the NSHCP instruction (NSHFCP $new,$expected,$masks)
NSHFCP $55,$30,$F0,$00,$50,$F0
  Shifts in a test vector that forces the last 8 cells (8..15) to 01010101 and all the first 8 cells (0..7) to 0
  Checks that cells (0..3) capture 0101 and cells (8..11) capture 0011

## Slide 10: Instructions for synchronisation with external test resources

## Slide 11: Instructions to control internal test resources and test flow

## Slide 12: Test program generation
The low abstraction level of the proposed instruction set makes “manual” test program development tedious and error-prone
It is highly desirable to have an automatic test program generation tool
However, our pedagogical objective would not be achieved if the small details of controlling the BS chain at bit-level were omitted