## Slide 1
Introduction to mixed-signal testing using the IEEE 1149.4 standard
J. M. Martins Ferreira
FEUP / DEEC - Rua dos Bragas
4050-123 Porto - PORTUGAL
Tel. 351-22-2041748 / Fax: 351-22-2003610
(jmf@fe.up.pt / http://www.fe.up.pt/~jmf)

## Slide 2: Objectives
To introduce the problem of testing mixed-signal circuits
To stress the fact that the 1149.1 standard can be extended (the 1149.4) to address mixed-signal circuits as well
To enable the student to acquire sufficient knowledge to understand and use the 1149.4 infrastructure

## Slide 3: Outline
The scope of 1149.4
Overview of the 1149.4 architecture
The Test Bus Interface Circuit (TBIC) and the Analog Boundary Modules (ABMs)
1149.4 in practice: Interconnect and parametric testing

## Slide 4: The IEEE 1149.4 standard
1149.4 is an extension of IEEE Std 1149.1 and defines the additional structures to be added to an 1149.1-conformant chip:
  An analog TAP (ATAP) with two pins (AT1, AT2)
  An internal analog test bus consisting of (at least) two lines (AB1, AB2)
  A test bus interface circuit (TBIC)
  Analog boundary modules (ABMs) on every analog function pin and optionally on other function pins

## Slide 5: The 1149.4 test infrastructure
Each analog I/O pin has an associated ABM that provides extended controllability and observability operations (enabling interconnect and parametric testing)
Analog test signals can be routed to or from the analog function pins through the TBIC and ATAP, which connect the internal test bus to the external test bus and ATE

## Slide 6: Structure of a basic 1149.4-conformant chip (1)
(the BS register cells of 1149.1 are now called DBMs)

## Slide 7: Structure of a basic 1149.4-conformant chip (2)
The operation of the 1149.4 infrastructure may be exemplified as follows:
  An analog input is externally provided to AT1 and the analog output is monitored at AT2
  AT1 and AT2 connect to the two-wire internal test bus consisting of AB1 and AB2
  From AB1 the signal can be routed to the core or to a function output pin
  Responses are routed to AB2 from the core or from a function input pin

## Slide 8: 1149.4 test register structure (1)

## Slide 9: 1149.4 test register structure (2)
The test register architecture of 1149.4 is entirely digital and essentially identical to the one defined by 1149.1
The BS register comprises the control registers of the TBIC (test bus interface circuit) and of the ABMs (analog boundary modules)
The control registers of the TBIC and ABMs define their respective operating modes

## Slide 10: The PROBE instruction
Besides the 3 mandatory 1149.1 instructions, 1149.4 defines a fourth mandatory instruction called PROBE:
  The selected data register is the BS register
  Each ABM will connect its pin to the core
  AT1 and AT2 are connected to AB1 and AB2
  Connection between analog pins and AB1 / AB2 is defined by the control register of each ABM
  Each digital boundary module (DBM) operates in transparent mode (as for S/P and BYPASS)

## Slide 11: BYPASS, S/P and EXTEST
Further to the description present in the 1149.1 standard, the following rules apply in 1149.4:
  BYPASS and S/P: i) AT1 / AT2 must be isolated from AB1 / AB2, as well as from all test voltage sources; ii) all analog function pins must be connected to the core circuit; iii) all analog function pins must be isolated from AB1 / AB2 and from all test voltage sources
  EXTEST: The ABM must disconnect the pin from the core

## Slide 12: 1149.4 optional instructions
Optional 1149.4 instructions are the same as for 1149.1 (INTEST, ID / USERCODE, RUNBIST, CLAMP and HIGHZ)
Further to the description present in the 1149.1 standard, the 1149.4 description of these instructions includes the rules defining the operating mode of the TBIC and ABMs

## Slide 13: The test bus interface circuit (TBIC)
The TBIC controls the connections between the ATAP (AT1 and AT2) and the internal test bus (at least two internal analog test lines — AB1 and AB2)
The ABMs and the TBIC assure the main feature of 1149.4 — the application and monitoring of analog test signals
The TBIC contains a switching structure and a control structure

## Slide 14: The TBIC switching structure (1)

## Slide 15: The TBIC switching structure (2)
The switching structure of the TBIC allows:
  AT1 or AT2 to be connected to VH or VL
  AT1 or AT2 to be connected to AB1 or AB2
  AT1 or AT2 to be connected to the internal voltage source VCLAMP
  A 1-bit representation of the voltage at AT1 or AT2 (as compared with the threshold voltage VTH)
Proper combination of these operating modes enable interconnect or parametric testing

## Slide 16: TBIC control structure (1)

## Slide 17: TBIC control structure (2)
The 4-bit TBIC control structure is part of the BS register and contains:
  A capture / shift stage: CALIBRATE, CONTROL, DATA1 and DATA2 (the 1-bit representation of the voltages at AT1 and AT2 is captured into the DATA1 and DATA2 bits)
  An update stage, which defines (together with the instruction decoder) the operating mode of the switching structure
  (TBIC cells are similar to typical 1149.1 BS cells, but lack the output multiplexer in the update stage)

## Slide 18: The analog boundary modules (ABMs) — The heart of 1149.4
The ABMs determine the flow of analog signals into and out of the function pins
Test signal application / capture through the ABMs is possible by combining serial access to the BS register and analog stimulus access to the ATAP
Each ABM contains a switching structure and a control structure

## Slide 19: ABM switching structure (1)

## Slide 20: ABM switching structure (2)
The switching structure of the ABMs allows:
  To disconnect the core from the function pin
  To drive the pin from AB1 (controllability)
  To drive AB2 from the pin (observability)
  To monitor a 1-bit representation of the voltage on the pin (compared with VTH)
  To connect VH or VL to the pin (interconnect test)
  To connect a reference quality voltage (VG) to the pin (useful for parametric measurements)

## Slide 21: ABM control structure (1)

## Slide 22: ABM control structure (2)
The 4-bit ABM control structure is part of the BS register and contains:
  A capture / shift stage: DATA, CONTROL, BUS1 and BUS2 (the 1-bit representation of the voltage at the pin is captured into the DATA stage)
  An update stage, which defines (together with the instruction decoder) the operating mode of the switching structure

## Slide 23: Simple interconnect testing with 1149.4
Interconnect testing (for open and short circuit faults) is similar as with 1149.1:
  In the case of digital pins, the data is loaded directly into the DBMs
  In the case of analog pins, the control codes that cause internally generated voltages (VH or VL) to be applied to the pin are loaded into the ABMs
  Test vector application and response capturing starts with the S/P instruction and deals only with digital data (both for digital and analog pins)

## Slide 24: Virtual probing with 1149.4: Impedance between pin and ground

## Slide 25: Impedance between pin and ground: Measurement procedure
Procedure:
  IT is applied through AT1, by way of switches S5 and SB1, to the unknown impedance (ZD)
  VT is measured at AT2, connected to ZD through switches SB2 and S6
  ZD is then given by ZD = VT / IT
Assumptions:
  ZV >> ZS6 + ZSB2 (negligible voltage drop in S6 and SB2)
  ZV + ZS6 + ZSB2 >> ZD (percentage of IT that does not flow through ZD is negligible)

## Slide 26: Virtual probing with 1149.4: Impedance between two pins (1)

## Slide 27: Impedance between two pins: Measurement procedure (1)
First part of the procedure:
  IT is applied through AT1, by way of switches S5 and SB1, to the unknown impedance (ZD), that has a fixed voltage VG applied at the other end
  VF1 is measured at AT2, connected to ZD through switches SB2 and S6
  The fact that VG is a quality reference voltage guarantees that the flow of IT will not cause any significant change in its voltage output

## Slide 28: Virtual probing with 1149.4: Impedance between two pins (2)

## Slide 29: Impedance between two pins: Measurement procedure (2)
Second part of the procedure:
  IT and VG are again applied to ZD
  VF2 is measured at AT2, connected to ZD through switches SB2 and S6
  ZD is then given by ZD = (VF1 - VF2) / IT
Assumptions:
  Regarding VF1, the same as between pin and ground
  Regarding VF2: ZV >> ZS6 + ZSB2 (negligible voltage drop in S6 and SB2 of the second P1149.4 component)
  (ZSG is very low, since VG is a quality reference voltage)

## Slide 30: 1149.4: Further information (1)

## Slide 31: 1149.4: Further information (2)