## Slide 1: An Introduction to Built-In Self-Test (BIST)
J. M. Martins Ferreira
FEUP / DEEC - Rua dos Bragas
4050-123 Porto - PORTUGAL
Tel. 351-22-2041748 / Fax: 351-22-2003610
(jmf@fe.up.pt / http://www.fe.up.pt/~jmf)

## Slide 2: Objectives
To reinforce the importance of BIST in the overall design for testability strategy
To present the procedures and the structures commonly used to implement BIST functions
To stress the importance of the BST infrastructure as a gateway to BIST functions and its role in the specification of hierarchical test strategies

## Slide 3: Contents
Overview of the BIST architecture at IC level
BIST functions and structures
  Combinational circuits
  Sequential circuits
  Macro-cells
Interface between BIST and the BST infrastructure
Design for testability and BIST in the Pentium Pro processor

## Slide 4: Built-In Self-Test
BIST is present when the resources required for the test execution (test pattern generation and application, response capture and evaluation) are internal to the circuit
BIST functions at IC level are normally implemented in hardware (firmware, in some cases) and tend to be implemented in software as we progress towards system level

## Slide 5: Built-In Self-Test
The main issues to consider are the following:
  Required fault coverage
  Acceptable test overhead (silicon area, degradation of circuit performance)
Cost / benefit analysis:
  Cost: test overhead and its implications during the design phase (time and resources - people / tools)
  The main benefits become visible when migrating from prototype to product, in the production test phase and in maintenance and diagnosis tasks

## Slide 6: BIST architecture at IC level (general overview)
BIST controller
TP generation and application
Response capture / evaluation
Internal circuit under test
Access to BIST functions
Primary inputs
Primary outputs

## Slide 7: BIST: TP generation and application - main problems
External generation of TPs to be stored in ROM: silicon area
Exhaustive / pseudo-exhaustive (when circuit partitioning is done previously) test: complexity of partitioning, test application time
Pseudo-random test pattern generation: fault simulation required (but the silicon area and design effort are small)

## Slide 8: BIST: response capture / evaluation - main problems
Responses stored in ROM and compared vector by vector: the required silicon area is again the main problem
Response compaction (several alternatives are available: transition counting, 1s counting, signature analysis, etc.): aliasing is possible (but the resources required and the test application time are far smaller)

## Slide 9: The BIST controller
The BIST controller is responsible for scheduling the several phases that comprise the execution of BIST (according to the type of circuit under test) and the operations that take place in each phase
This block constitutes the interface between external test resources and the BIST functions and plays an important role in the definition of the overall system BIST strategy

## Slide 10: BIST of combinational circuits
Any of the techniques previously referred may be used (be it for TP generation / application or for response capture / evaluation)
Pseudo-random TP generation and response compaction by signature analysis are common BIST solutions for this type of circuits

## Slide 11: Combinational circuits: TP generation / application
Pseudo-random TP generation via an LFSR (Linear Feedback Shift Register) for a 2:1 multiplexer

## Slide 12: Combinational circuits: TP generation / application
Recommended exercises:
  What connections should be made between the circuit under test and the LFSR?
  What is the required number of test clock cycles?
  What should be the initial value in the LFSR outputs (Q0 to Q3)?
  Would it be possible to use a 3-bit LFSR?
  How do the pseudo-random and exhaustive TP generation alternatives compare in terms of test overhead?

## Slide 13: Combinational circuits: response capture / evaluation
Response compaction (by signature analysis) via an LFSR for the 2:1 multiplexer

## Slide 14: Combinational circuits: response capture / evaluation
Recommended exercises :
  What connections should be made between the circuit under test and the LFSR?
  What is the required number of test clock cycles?
  What should be the initial value in the LFSR outputs?
  Will the number of bits in the signature influence the probability of aliasing?
  Present an example showing the aliasing effect

## Slide 15: Combinational circuits: response capture / evaluation
Other compaction alternatives:
  Transition counting
  Syndrome counting (number of 1s)
Recommended exercise: considering that an exhaustive test is applied to the 2:1 multiplexer, determine the expected result for the three alternatives referred. In which case will the probability of aliasing be higher?

## Slide 16: BIST of sequential circuits
With the exception of deterministic testing, using TPs stored in ROM, the remaining techniques presented for TP generation / application (exhaustive or pseudo-exhaustive, pseudo-random TP generation) are not applicable with sequential circuits
Will response compaction, by the methods presented (e.g. signature analysis), be applicable in this case?

## Slide 17: BIST of sequential circuits
The design for testability techniques commonly used (namely scan design) eliminate the sequential nature of the circuit and enable the usage of the BIST methods considered previously
The memory elements (FF) may in fact integrate the structures implementing pseudo-random TP generation and response compaction via signature analysis

## Slide 18: BIST of macro-cells
This hierarchical level helps to solve the test problems associated with complex blocks available to ASIC designers
Each macro-cell comprises its own BIST resources, according to the methods already described, which now have to be integrated into the overall BIST strategy defined for the upper hierarchical levels

## Slide 19: BIST of low / medium complexity macro-cells
Low / medium complexity macro-cells, such as memory blocks, require relatively homogeneous BIST resources:
  BIST of ROM blocks may be done by reading each memory address and compacting its contents into a signature
  RAM blocks are medium complexity macro-cells and their BIST functions take into account several fault models

## Slide 20: BIST of higher complexity macro-cells
The availability of higher complexity macro-cells (e.g. a microcontroller), integrating different circuit blocks, calls for a standard interface facilitating access to the BIST functions present
The heterogeneous nature of these BIST functions and the need to protect intellectual property rights led to the development of an IEEE standard in this area

## Slide 21: BIST of mega-cells: the IEEE P1500 proposed standard
The IEEE P1500 proposes a standard
  Addressing ICs “containing embedded cores, i.e. reusable mega-cells”
  “Independent of the underlying functionality of the IC or its individual embedded cores”
  Creating the “testability requirements for detection and diagnosis (...), while allowing for ease of inter-operability of cores originated from distinct sources”
  “Usable for all classes of digital cores including hierarchical ones”

## Slide 22: Interface between BIST and the BST infrastructure
The BST infrastructure facilitates access to the BIST functions present in an IC, since:
  The TAP provides access to the BIST controller, which no longer requires dedicated test pins
  The IEEE 1149.1 standard defines an optional instruction called RUNBIST, which standardises access to the BIST functions present, independently of the manufacturer and functionality of the circuit

## Slide 23: Architecture of a BST component with BIST
The BIST controller at IC level uses the BIST bus to interface the BST infrastructure and the BIST structures present

## Slide 24: Architecture of a BST component with BIST
The BIST controller is necessary to schedule the operation of the BIST functions present
The BST register can also be used for TP generation / application and response capture / evaluation, e.g. for pseudo-random TP generation and response compaction by signature analysis (using modified BS cells)

## Slide 25: The RUNBIST instruction revisited
The main specifications of the IEEE 1149.1 standard in relation to RUNBIST are as follows:
  Self-test modes of operation shall execute only when the TAP controller is in the Run Test / Idle state
  A duration shall be specified for the self-test (number of test clock cycles)
  The test data register selected by RUNBIST shall contain the self-test result after the specified number of test clock cycles were applied
  ...

## Slide 26: The RUNBIST instruction revisited
As a simple application example, the reader is invited to design the BIST structures for a BST component containing the 2:1 multiplexer previously considered
Suggestion: reuse the BS cells to implement the structures required for pseudo-random TP generation and response compaction by signature analysis

## Slide 27: Hierarchical BIST
BST components supporting BIST facilitate the implementation of a hierarchical BIST strategy
The printed circuit board should in this case contain a BIST controller (a dedicated component for this purpose), which will be responsible for the implementation of the test protocol presented for BST boards (infrastructure test, interconnection test, component test)

## Slide 28: Hierarchical BIST
The existence of a BST infrastructure in the board test controller enables the implementation of a hierarchical self-test strategy in which the IEEE 1149.1 standard is used both at board and system level
However, and since BST was developed to facilitate the structural testing of digital printed circuit boards, its extension to system level faces some restrictions (mention one)

## Slide 29: Hierarchical BIST: IEEE 1149.5 and IEEE P1500
IEEE 1149.5 (Standard for Test and Maintenance Bus) defines a system level test bus comprising 4+1 lines (MMD, MSD, MCTL, MCLK, MPR)
There are also other solutions proposed with the objective of enabling the use of the IEEE 1149.1 standard at system level, with the advantage of optimising the test resources required

## Slide 30: Design for testability and BIST in the Pentium Pro processor
A suitable trade-off solution has to be found, concerning the percentage of silicon area dedicated to testability and BIST functions
Design for testability can not be excluded, but we must keep in mind that the silicon area used for this purpose could instead be used to improve circuit performance, therefore leading to higher probability of commercial success

## Slide 31: Design for testability and BIST in the Pentium Pro processor
The main requirements that led to the design for testability / BIST functions present in the Pentium Pro processor were the following:
  “Have zero performance impact”
  “Have minimal die area impact”
  “Be multiuse features wherever possible (supporting component debug, production test, and so on)”
  “Be designed in from the start (that is, coded and validated in the register-transfer-level model)”

## Slide 32: Design for testability and BIST in the Pentium Pro processor
Reference: A. Carbine, D. Feltham, “Pentium Pro Processor Design for Test and Debug,” IEEE Design and Test of Computers, July-September 1999, pp. 77-82.

## Slide 33: Design for testability and BIST in the Pentium Pro processor
The Pentium Pro BST infrastructure supports seven public instructions and “many more private instructions” to support test and debug
Scan-out provides observability of more than 2.000 internal nodes (snapshot / signature)
Debug stops the processor and enables an interactive test mode, following which the processor may return to the normal execution mode

## Slide 34: Design for testability and BIST in the Pentium Pro processor
The Internal breakpoint mechanism can be set up for several internal events and for the subsequent debugging actions
Microcode update enables the temporary modification of microcode sections to facilitate test and debug in early silicon
The IDDQ mode uses a private BST instruction to disable all devices that draw static current and enable IDDQ tests

## Slide 35: Design for testability and BIST in the Pentium Pro processor
Main features of the Pentium Pro BIST functions:
  There is a self-test routine that is “primarily targeted at achieving high toggle coverage for burn-in testing”
  LFSRs were used to implement BIST structures for “several inaccessible programmable logic arrays”
  The L2 PBIST is a programmable array test pattern generator to facilitate the production test of the L2 cache memory (256 K)

## Slide 36: Design for testability and BIST in the Pentium Pro processor
Production test effectiveness is ultimately measured by the number of defective components that are shipped to customers (in parts per million) and not by fault coverage figures
Design for testability and BIST in the Pentium Pro required 4% of the CPU silicon area and 6% of the L2 cache memory area, with “no negative impact on processor performance, either in clock frequency or instructions per clock”